## Slide 1: NEW SPRINT
Sprint | WBGOPSMMYY
Particulars | To Check weighment Differences / Truck Variation, Prevent Problems, Check Flow Meters Readings with actual loadings & identify variations, SF / IVC65 - No flow meter, Accuracy Reading by using nearest weighing scales, check weigh bridges variation, check options for No man weighbridge, Check for sensors to identify correct placement of vehicles to avoid manipulation, packing material weight calculation’s with concerned Dept., Prevent Excess Bags loading, Random weighments by production to avoid excess fillings etc. Collection of suggestions from all Departments
Start Date | 01st Day of Month
End Date | Last Day of Month

## Slide 2: SCRUM TEAM
Scrum Master | Scrum Master
Product Owner | Commercial Incharge
Developers | 1) Weighbridge 2) Barrel Filling 3) New Beeding 4) Flacker 5) FMCG & Lauric Fats 6) Instrumentation 7) Logistics 8) Pharma

## Slide 3: SCRUM EVENTS
Sprint | Entire Month
Sprint Planning | 01st of Month
Daily Scrum | 15 Minutes – Daily
Sprint Review | 25th of Month
Sprint Retro | Last day of Month

## Slide 4: Previous Observations
S.No | Month | Division Description |  |  |  |  |  |  | Grand Total of Loss Value
 |  | Animal Health & Nutr -Loss Value | BF - Bakery Fats -Loss Value | BF - Industrial Comp | FMCG - Edible Oils -Loss Value | LF_Lauric Fat -Loss Value | OC - Oleo Chemicals -Loss Value | PH - Pharma -Loss Value | 
1 | Apr-23 | 8,196 | - | - | 20,941 | 20,847 | 47,105 | - | 97,089
2 | May-23 | 1,640 | - | - | 5,115 | 4,534 | 98,595 | 9,113 | 118,996
3 | Jun-23 | 8,505 | 1,999 | - | - | 5,334 | 60,251 | 13,214 | 89,303
4 | Jul-23 | 5,340 | 3,685 | - | - | 7,069 | 33,753 | 4,831 | 54,678
5 | Aug-23 | 27,141 | - | - | 23,916 | 7,016 | 32,795 | - | 90,870
6 | Sep-23 | -1,910 | - | - | 11,488 | 8,530 | -7,464 | - | 10,645
7 | Oct-23 | - | 3,366 | - | 5,851 | - | 8,557 | 10,752 | 28,527
8 | Nov-23 | 29,743 | - | - | 979 | - | 27,111 | - | 57,833
9 | Dec-23 | 30,996 | 3,696 | - | 16,583 | 5,144 | 93,953 | - | 150,372
10 | Jan-24 | 43,685 | - | 3,061 | 3,621 | 5,500 | 129,058 | 12,642 | 197,567
11 | Feb-24 | 45,519 | - | 5,602 | 3,770 | - | 21,419 | 1,750 | 78,060
12 | Mar-24 | 35,727 | - | - | 1,186 | 6,311 | 45,692 | 3,427 | 92,343
 | Grand Total | 234,582 | 12,746 | 8,663 | 93,452 | 70,285 | 590,825 | 55,728 | 1,066,282

## Slide 5
IDENTIFIED REASONS
FOR WEIGHMENT VARIATIONS

## Slide 6
WEIGH BRIDGE VARIATIONS
WEIGHING SCALE TOLERANCE
FILLING ERRORS

## Slide 7
WEIGH BRIDGE HAS BEEN VERIFIED AND LOCAL WEIGHMENTS ALSO CHECKED.
NO MAJOR VARIATION

## Slide 8
IDENTIFIED WEIGHING SCALES ARE HIGHER TOLERANCE AND LAST 3RD DIGIT IS NOT VISIBLE AND LESSER ACCURACY

## Slide 9
LIST OF WEIGHING SCALES - 3F INDUSTRIES LIMITED. KRISHAPATNAM |  |  |  |  |  |  |  |  |  | 
S.No. | WEIGHING SCALES |  |  |  |  | Location | Purpose | Filling Capacity | Nearest Weighing Scale | Digits
 | Make | Model | S.NO | Capacity | Accuracy |  |  |  |  | 
1 | LCGC | PUE C315 | 673964 | 1500 kg | 200 gr | Soap Plant | Soap noodles jumbo bag | 1000 Kg. | 1500 kg | 
2 | ESSAE | DS-451 | 45119291081 | 1000 Kg | 200 gr | New beads | Beads Jumbo bags | 650 Kg. | 1000 kg | 
3 | ESSAE | DS-451 | 45112119314 | 600 kg | 50 gr | Oleo | Glycerine barrels filling | 250 Kg. | 300 kg | 3 digits
4 | ESSAE | SI-850 | SI81020313725 | 600 kg | 50 gr | Soap plant | Glycerine barrels filling | 250 Kg. | 300 kg | 3 digits
5 | ESSAE | SI-850 | SI81020313726 | 600 kg | 50 gr | Pharma plant | Glycerine barrels filling | 250 Kg. | 300 kg | 3 digits
6 | ESSAE | DS-451 | 45112119181 | 300 kg | 20 gr | Oleo | Glycerine barrels filling | 250 Kg. | 300 kg | 
7 | ESSAE | SI-850 | SI85022380493 | 300 kg | 50gr | Soap palnt | Dimmer barrles filling | 200 Kg. | 300 kg | 3 digits
8 | ESSAE | SI-850 | SI85022380494 | 300 kg | 50gr | Soap palnt | Dimmer barrles filling | 200 Kg. | 300 kg | 3 digits
9 | ESSAE | DS-451 | 45113122897 | 150 kg | 10 gr | Soap plant | Soap noodles | 25 / 50 Kgs. | 60 kg | 
10 | ESSAE | DS-451 | 45113122898 | 150 kg | 10 gr | Soap plant | Steric acid bags | 25 / 50 Kgs. | 60 kg | 

## Slide 10
LIST OF WEIGHING SCALES - 3F INDUSTRIES LIMITED. KRISHAPATNAM |  |  |  |  |  |  |  |  |  | 
S.No. | WEIGHING SCALES |  |  |  |  | Location | Purpose | Filling Capacity | Nearest Weighing Scale | Digits
 | Make | Model | S.NO | Capacity | Accuracy |  |  |  |  | 
11 | ESSAE | DS-451 | 45113122899 | 150 kg | 10 gr | Soap plant | Steric acid bags | 25 / 50 Kgs. | 60 kg | 
12 | ESSAE | DS-451 | 45113122900 | 150 kg | 10 gr | Oleo - PLC | catylist mixing | - | - | 
13 | ESSAE | DS-451 | 45118260490 | 150 kg | 10 gr | New beads | Steric acid bags | 25 / 50 Kgs. | 60 kg | 
14 | ESSAE | DS-451 | 45118260491 | 150 kg | 10 gr | New beads | Beads bags | 25 Kgs. | 30 kg | 
15 | ESSAE | DS-451 | 45122380613 | 150 kg | 10 gr | Dimmer plant | chemical add | - | - | 
16 | ESSAE | DS-451 | 45120311415 | 100 kg | 10 gr | Soap plant | Soap noodles | 25 / 50 Kgs. | 60 kg | 
17 | ESSAE | DS-451 | 45120311416 | 100 kg | 10 gr | New beads | Steric acid bags | 25 / 50 Kgs. | 60 kg | 
18 | ESSAE | SI-810 | SI81016189393 | 60 kg | 5 gr | Soap plant | Loading point | 25 / 50 Kgs. | 60 kg | 3 digits
19 | LCGC | PUE C315-60 SS | 662239 | 60 kg | 5 gr | Pharma plant | Pharma 25kg bags | 25 kgs. | 30 kg | 
20 | ESSAE | SI-810 | SI81017224054 | 50 Kg | 5 gr | Packing plant | 1Lt pouch box conveyor -1 | 1 Ltr. | 30 kg | 3 digits

## Slide 11
LIST OF WEIGHING SCALES - 3F INDUSTRIES LIMITED. KRISHAPATNAM |  |  |  |  |  |  |  |  |  | 
S.No. | WEIGHING SCALES |  |  |  |  | Location | Purpose | Filling Capacity | Nearest Weighing Scale | Digits
 | Make | Model | S.NO | Capacity | Accuracy |  |  |  |  | 
21 | ESSAE | SI-850 | SI85023392246 | 50 kg | 5gr | Packing plant | 1Lt pouch box conveyor -2 | 1 Ltr. | 30 kg | 3 digits
22 | ESSAE | SI-850 | SI85023392247 | 50 kg | 5gr | Lauric fats | 15 kg tins | 15 Kgs. | 30 kg | 3 digits
23 | ESSAE | SI-850 | SI85023392248 | 50 kg | 5gr | Lauric fats | 15kg tins | 15 Kgs. | 30 kg | 3 digits
24 | TULAMAN | EPC | HT19EP03055170 | 30 kg | 5 gr | Lauric fats | 15kg Tins | 15 Kgs. | 30 kg | 
25 | TULAMAN | EPC | HT19EP03055171 | 30 kg | 5 gr | Lauric fats | 15kg Tins | 15 Kgs. | 30 kg | 
26 | LCGC | WLC60/C2/K | 630064 | 30 kg | 1 gr | Lauric fats | 15kg Tins | 15 Kgs. | 30 kg | 
27 | LCGC | WLC60/C2/K | 673958 | 30 kg | 1 gr | New beads | 25 kg beads bags | 25 kgs. | 30 kg | 
28 | ESSAE | DS-450 SS | DS45021344492 | 15 Kg | 1gr | RO plant | chemical mixing | - | - | 
29 | TULAMAN | ETP | HT19ET01054989 | 10 Kg | 1 gr | Boiler | chemical mixing | - | - | 
30 | ESSAE | DS-451 HP | 45117223734 | 6000 gr | 0.5 gr | Qc lab / Soap plant | Chemical add | - | - | 

## Slide 12
LIST OF WEIGHING SCALES - 3F INDUSTRIES LIMITED. KRISHAPATNAM |  |  |  |  |  |  |  |  |  | 
S.No. | WEIGHING SCALES |  |  |  |  | Location | Purpose | Filling Capacity | Nearest Weighing Scale | Digits
 | Make | Model | S.NO | Capacity | Accuracy |  |  |  |  | 
31 | ESSAE | DS-451 HP | 45117224189 | 6000 gr | 0.5 gr | Packing plant | 1 Kg pouches | 500 ml/ 1 Ltr. | 2 kg | 
32 | ESSAE | DS-451 HP | 45117224190 | 6000 gr | 0.5 gr | Packing plant | 1 kg pouches | 500 ml/ 1 Ltr. | 2 kg | 
33 | ESSAE | DS-450 SS | 45018268071 | 6000 gr | 0.5 gr | Packing plant | 1 kg pouches | 500 ml/ 1 Ltr. | 2 kg | 
34 | ESSAE | DS451 | DS45122356820 | 6000 gr | 0.5 gr | New ETP | chemical add | - | - | 
35 | LCGC | PUE C315-6 SS | 662238 | 6kg | 1 gr | Pharma Plant | 5kg Sample packing | - | - | 
36 | LCGC | WTC 600 | 670904 | 600 gr | 0.01 gr | Pharma Plant | Analysis | - | - | 
37 | LCGC | AS 82/220.R2 | 640974 | 82/220 gr | 0.01/0.1 mg | Pharma Plant | Analysis | - | - | 
38 | JASUBHAI | UBM | 138002010055 | 100 kg | 10 gr | New Beads | Bag check weigher | - | - | 
39 | METTLER | IND570 | 2744160004 | 30Kg | 5gr | Lauric fats | Box check weigher | - | - | 3 digits
40 | ESSAE | DX-451 | DX45123410684 | 3 kg | 0.2 gr | Packing | 1 Kg pouches |  |  | 
41 | ESSAE | DX-451 | DX45123410681 | 3 kg | 0.2 gr | Pharma Plant | Analysis |  |  | 

## Slide 13
S.No | LOCATION | CAPACITY (kg) | MAKE | MODEL | S.NO | E - VALUE | LIFE | REMARKS
1 | New Beads - JUMBO- W.SCALE | 1,000 | ESSAE | DS-451 | 45119291081 | 200 gr | 5 years | Keyboard problem
2 | OLEO | 600 | ESSAE | SI-850 | SI850623000163 | 50 gr | 12 years | Platform damaged
3 | OLEO | 300 | ESSAE | DS-451 | 45112119181 | 20 gr | 12 years | Platform damaged
4 | SOAP PLANT | 150 | ESSAE | DS-451 | 45113122897 | 10 gr | 11 years | checked and found ok
5 | SOAP PLANT | 150 | ESSAE | SI-850 | SI850623000164 | 10 gr | 11 years | checked and found ok
6 | SOAP PLANT | 150 | ESSAE | DS-451 | 45113122899 | 10 gr | 11 years | Platform lug thread damaged
7 | OLEO | 150 | ESSAE | DS-451 | 45113122900 | 10 gr | 11 years | Platform rust
8 | PACKING | 60 | ESSAE | SI-810 | SI81016189393 | 5 gr | 8 years | Platform lugs are not available
9 | SOAP PLANT | 150 | ESSAE | DS-451 | 45118260490 | 10 gr | 6 years | checked and found ok
10 | SOAP PLANT | 150 | ESSAE | DS-451 | 45118260491 | 10 gr | 6 years | checked and found ok
11 | PACKING | 50 | ESSAE | SI-810 | 81017224054 | 5 gr | 7 years | checked and found ok
12 | QC Lab (SOAP PLANT) | 6 | ESSAE | DS-451 HP | 45117223734 | 0.5 gr | 7 years | checked and found ok
13 | PACKING | 6 | ESSAE | DS-451 HP | 45117224189 | 0.5 gr | 7 years | checked and found ok
14 | PACKING | 6 | ESSAE | DS-451 HP | 45117224190 | 0.5 gr | 7 years | checked and found ok
15 | PACKING | 6 | ESSAE | DS-450 SS | 45018268071 | 0.5 gr | 6 years | checked and found ok
16 | Pharma Plant | 600 | ESSAE | SI-810 | 81020313725 | 50 gr | 4 years | display and platform wet , to be keep at sunlight
17 | New beads | 600 | ESSAE | SI-810 | 81020313726 | 50 gr | 4 years | checked and found ok
18 | New beads | 100 | ESSAE | DS-451 | 45120311415 | 10 gr | 4 years | checked and found ok
19 | New beads | 100 | ESSAE | DS-451 | 45120311416 | 10 gr | 4 years | checked and found ok
20 | RO Plant | 15 | ESSAE | DS-450 SS | DS45021344492 | 1gr | 3 years | Platform and display rust formed
21 | New ETP | 6 | ESSAE | DS451 | DS45122356820 | 0.5 gr | 2 years | checked and found ok
22 | Dimer plant | 300 | ESSAE | SI-850 | SI85022380493 | 50gr | 2 years | checked and found ok
23 | Dimer plant | 300 | ESSAE | SI-850 | SI85022380494 | 50gr | 2 years | checked and found ok
24 | Dimer plant | 150 | ESSAE | DS451 | DS45122380613 | 10gr | 2 years | checked and found ok
25 | PACKING | 50 | ESSAE | SI-850 | SI85023392246 | 5gr | 1 year | checked and found ok
26 | Lauric Fats | 50 | ESSAE | SI-850 | SI85023392247 | 5gr | 1 year | checked and found ok
27 | PACKING | 50 | ESSAE | SI-850 | SI85023392248 | 5gr | 1 year | checked and found ok
28 | Lauric Fats | 100 | ESSAE | SI-850 | SI85023392245 | 10gr | 1 year | checked and found ok
29 | Packing | 3000gr | ESSAE | DX-451 | DX45123410684 | 0.2gr | 6 months | 3 sides to be closing head and platform
30 | Pharma Plant | 3000 gr | ESSAE | DX-451 | DX45123410681 | 0.2 gr | 6 months | checked and found ok
31 | Pharma Plant | 220 gr | ESSAE | AX-220 | AX22023409548 | 0.001gr | 6 months | checked and found ok
32 | Pharma Plant | 100 kg | ESSAE | DX-451 | DX45123409658 | 10 gr | 6 months | checked and found ok
33 | Pharma Plant | 100 kg | ESSAE | DX-451 | DX45123409659 | 10 gr | 6 months | checked and found ok
34 | Pharma Plant | 100 kg | ESSAE | DX-451 | DX45123409657 | 10 gr | 6 months | checked and found ok

## Slide 14
REQUEST ALL TEAM MEMBERS TO MAINTAIN S.O.P BY CHECKING WEIGHMENTS OF
ONE IN 10
TO FIND OUT DEVIATIONS

## Slide 15
The following quotes
Taken for weighing scales for reviewing with
Senior Management and take guidance

## Slide 16
SL. NO. | DESCRIPTION |  |  | BASICPRICE* PER UNIT(Rs.)
01 | MODEL: SI-850 SINGLE LOAD CELL-SS304 MOC, ETHERNET (10,890) CAPACITY: 60 kg ACCURACY:5 GMS PLATTTER SIZE: 450X550 MM PLATTER MOC: SS 304, FRAME MOC: SS 304 |  |  | 82,980-00
02 | MODEL: SI-850 BENCH TYPE-SS304 MOC, ETHERNET (10,890) CAPACITY: 3 kg ACCURACY:0.2 GMS PLATTTER SIZE: 360X280 MM PLATTER MOC: SS 304, FRAME MOC: SS 304 |  |  | 65,870-00
03 | OPTIONS:3 COLOUR TOWER LAMP KIT SI-850 |  |  | 3,870-00 (NO DISCCOUNT)
Note: We are here with offering 20% discount on above basic price. Now we request you to kindly release your valuable purchase order in favourof M/S ESSAE-TERAOKA PVT LTD,PLOT NO.4B, BOMMASANDRA,IDA,BANGLURU. COMMERCIAL TERMS |  |  |  | 
01 |  | GST/TAXES | 18% GST TAXES EXTRA ON BASIC | 
02 |  | Freight | PAID | 
03 |  | Delivery | 3 TO 4 WEEKS | 
04 |  | Payment Terms | 100% Advance | 
05 |  | Validity | 30 DAYS | 
06 |  | Warranty | One year from the date of invoice | 

## Slide 17
SL. NO. | DESCRIPTION |  |  | BASICPRICE* PER UNIT(Rs.)
01 | MODEL: SI-850 SINGLE LOAD CELL-SS304 MOC,WITH MS TOP ROLLER & ETHERNET (10,890) CAPACITY: 100 kg ACCURACY:5 GMS PLATTTER SIZE: 550X650 MM PLATTER MOC: SS 304, FRAME MOC: SS 304 |  |  | 1,05,680-00
02 | OPTIONS:3 COLOUR TOWER LAMP KIT SI-850 |  |  | 3,870-00 (NO DISCCOUNT)
Note: We are here with offering 20% discount on above basic price. Now we request you to kindly release your valuable purchase order in favourof M/S ESSAE-TERAOKA PVT LTD,PLOT NO.4B, BOMMASANDRA,IDA,BANGLURU. COMMERCIAL TERMS |  |  |  | 
01 |  | GST/TAXES | 18% GST TAXES EXTRA ON BASIC | 
02 |  | Freight | PAID | 
03 |  | Delivery | 3 TO 4 WEEKS | 
04 |  | Payment Terms | 100% Advance | 
05 |  | Validity | 30 DAYS | 
06 |  | Warranty | One year from the date of invoice | 

## Slide 18
THANK YOU